## Slide 1: Indoor Location using Wi-Fi Signals
Guilherme Ribeiro

## Slide 2: Context
Smartphones are very common now a days
People are used to use GPS based apps for location and route guide

## Slide 3: Problem
GPS does not work inside buildings, shopping malls, airports etc.
How to overcome this issue?
  Beacons
  Wi-Fi signals

## Slide 4: Data
Universitat Jaume I
3 Buildings
4 or 5 floors
110.000m²

## Slide 5: Data
20 different users
25 different smartphone devices
529 attributes
  520 Wireless Access Points (WAP)
    Range: -104dBm to 0dBm
  Building, Floor, Latitude, Longitude…
19.937 rows of training records
  Fixed positions
1.111 rows of validation records
  Random positions

## Slide 6: Data - Training

## Slide 7: Data - Validation

## Slide 8: Approach/Analysis
Divide and conquer
  First, find the Building which a person is
  Then, knowing the Building, find the Floor, Latitude and Longitude
Find the best algorithm for each problem based on its metrics
  Random Forest
  SVM
  K-NN
Tune the algorithms selected to find their optimal parameters

## Slide 9: Approach/Analysis
Replace the +100 values for -105 for all WAPs
Filter all WAPs with low variance
Sample the data in a representative way
  Building prediction
    10 points per floor per building
  Floor, Latitude and Longitude prediction
    Max of 5 points per room

## Slide 10: Results
Building Prediction
  SVM was chosen
 |  | Reference |  | 
 |  | 0 | 1 | 2
Prediction | 0 | 536 | 0 | 0
 | 1 | 0 | 307 | 0
 | 2 | 0 | 0 | 268
Accuracy | Kappa
1 | 1

## Slide 11: Results
Floor predictions
Accuracy | Kappa
0.9720149 | 0.9603814
 |  | Reference |  |  | 
 |  | 0 | 1 | 2 | 3
Prediction | 0 | 72 | 1 | 1 | 0
 | 1 | 3 | 207 | 3 | 0
 | 2 | 3 | 0 | 159 | 2
 | 3 | 0 | 0 | 2 | 83
Building 0
Building 1
Accuracy | Kappa
0.8078176 | 0.7280044
 |  | Reference |  |  | 
 |  | 0 | 1 | 2 | 3
Prediction | 0 | 26 | 19 | 0 | 0
 | 1 | 1 | 95 | 1 | 0
 | 2 | 3 | 28 | 83 | 3
 | 3 | 0 | 1 | 3 | 44
Accuracy | Kappa
0.9328358 | 0.9087625
 |  | Reference |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4
Prediction | 0 | 21 | 1 | 0 | 0 | 2
 | 1 | 3 | 107 | 1 | 0 | 0
 | 2 | 0 | 3 | 52 | 0 | 0
 | 3 | 0 | 0 | 1 | 37 | 4
 | 4 | 0 | 0 | 0 | 3 | 33
Building 2
Random Forest
Random Forest
SVM

## Slide 12: Error Analysis
Floor prediction for Building 1

## Slide 13: Results
Latitude and Longitude predictions
Building 0
Building 1
Building 2
Latitude |  | 
RMSE | R² | MAE
5.1132279 | 0.9749703 | 3.5007124
K-NN
K-NN
Random Forest
Longitude |  | 
RMSE | R² | MAE
6.1092082 | 0.9479081 | 4.2998259
Latitude |  | 
RMSE | R² | MAE
11.7345699 | 0.9002153 | 8.7780720
Longitude |  | 
RMSE | R² | MAE
9.2490759 | 0.9606184 | 7.0192680
Latitude |  | 
RMSE | R² | MAE
9.7121582 | 0.8910852 | 6.8210913
Longitude |  | 
RMSE | R² | MAE
11.2548716 | 0.8752998 | 7.4059147

## Slide 14: Error Analysis
Latitude prediction error in Building 2

## Slide 15: Conclusions
We can get 100% accuracy in validation set for building prediction
We need further investigation on building 1 for floor prediction
  Pre and post processing together could improve the model
Post processing on Latitude and Longitude based on building boundaries might decrease the errors

## Slide 16: Appendix
WAPs signals strength distribution

## Slide 17: Appendix
WAPs signals strength distribution
Phone 17
Phone 19